## Slide 1
AFTER THE DEMO MEETING
Aggregation, Orchestration
and V2G
How many small energy sources become one dependable supply,
with and without vehicles, and what it means for DEG / IES
Sanjay S · MS/EAC11-EM · September 2026

## Slide 2
CONTEXT
What the demo meeting asked us to think about
Source: Questions raised by the team during the P2P demo review
2
1 Beyond one-to-one
Not one person selling a few kWh to another, but an aggregator with a bulk contract to a DISCOM or large buyer.
2 Many vehicles, one supply
Orchestrating many EVs through V2G. Who are the actors, and who actually needs this?
3 What already exists
V2G in Europe (Germany), in India, and what Bosch itself has reached.
4 What if it goes wrong
A bid is accepted but never supplied. A buyer hoards offers to disturb the network. The solar fails.
5 How V2G physically works
Vehicle to charger to grid. How does an aggregator with a contract really get the power?
6 Where it fits in DEG / IES
And what about plain aggregation, before V2G is even involved?
The rest of this deck answers these six, in this order.

## Slide 3
THE ANSWER IN ONE PICTURE
Small resources, one aggregator, one firm offer
Source: Synthesis of the two research passes; layers as described on slides 9 and 13
3
Marketplace and contract layer: Beckn / UEI / DEG (discover, agree, settle)
Many small resources
Home rooftop solar
Home batteries
EVs on chargers
Smart air-conditioners
Each 1 to 10 kW
Aggregator
Pools them into one bid
Forecasts who is available
Sends live control signals
Measures what was delivered
DISCOM or market
Needs a large, firm block
Buys MW, not kW
Pays for what is delivered
Charges for any shortfall
control
one offer
payment
share
Device layer: OCPP 2.1 · ISO 15118-20 · IEEE 2030.5 · OpenADR
With vehicles that can export power, this is called V2G. Without them, it is plain aggregation. The mechanics are the same.

## Slide 4
HOW TO READ THIS DECK
Every claim is labelled by how sure we are
Source: Method used across both research passes
4
VERIFIED
We read the official or primary source ourselves.
REPORTED
Comes from a secondary source, such as a news article or summary.
INFERENCE
Our own reasoning or calculation. Not from a source.
EXAMPLE
An illustration with made-up numbers, to explain an idea.
PROPOSED
What we suggest building. Does not exist yet.
Where something could not be verified, the deck says so
instead of guessing.
A
Who is who
Entities and terms
B
Aggregation
With and without V2G
C
V2G
Physical chain and actors
D
Risks
Non-delivery, hoarding, failure
E
Bosch and India
What exists, what is missing
F
Proposal
Where we go next

## Slide 5
A WHO IS WHO
Power-sector basics in six boxes
Source: Standard definitions; Indian context from the Ministry of Power and REC material used earlier in this project
5
kW and kWh
kW is how fast power flows. kWh is how much energy over time. A 5 kW charger running 2 hours delivers 10 kWh.
MW
1 MW is 1,000 kW. Grid markets work at this scale, not at the scale of one home.
DER
Distributed Energy Resource: any small source, store or flexible load near the customer. Solar roof, home battery, EV, air-conditioner.
DISCOM
Distribution company. Runs the local wires and sells power to homes and businesses.
Transmission vs distribution
Transmission is the high-voltage long-distance grid. Distribution is the local network that reaches customers.
Regulator
A government body that sets the rules and tariffs everyone else must follow.

## Slide 6
A WHO IS WHO
Regulators and grid operators that appear in this deck
VERIFIED
Source: Regulation texts and operator pages cited on the Sources slides; descriptions are general background
6
CERC
Central Electricity Regulatory Commission, India. Regulates inter-state power and national markets. Its 2022 Ancillary Services rules allow aggregated reserve providers, with a 1 MW minimum.
RERC
Rajasthan Electricity Regulatory Commission. State regulator whose 2026 Demand Flexibility Regulations recognise registered aggregators.
CEA and BIS
Central Electricity Authority (technical planning and standards) and Bureau of Indian Standards (product standards, such as EV chargers).
FERC
Federal Energy Regulatory Commission, USA. Its Order 2222 opens wholesale markets to aggregations of small resources.
PJM
A large US regional grid operator running big power and capacity markets. Its manual sets credit limits and a non-performance charge.
Amprion
One of Germany's four transmission grid operators. Its balancing-market rules set a 1 MW minimum bid.

## Slide 7
A WHO IS WHO
Indian utilities and programme partners
VERIFIED
Source: ISGF V2G demonstration release (May 2026); DEG demand-flex devkit; general background
7
TPDDL
Tata Power Delhi Distribution Ltd. A Delhi DISCOM. Plays the utility buyer in DEG's demand-flex example, and a partner in the 2026 V2G demo.
BSES Rajdhani (BRPL)
A Delhi DISCOM serving the south and west of the city. Partner in the May 2026 V2G demonstration.
BSES Yamuna (BYPL)
A Delhi DISCOM serving the central and east of the city. Also a partner in the 2026 V2G demonstration.
ISGF
India Smart Grid Forum. A public-private, not-for-profit body promoting smart grids. It led India's first V2G demonstration.
ANERT
Kerala government agency for new and renewable energy. A partner in the same demonstration.
Ministry of Power and REC
The Ministry issued the 2024 EV charging guidelines. REC Limited is the nodal agency for India Energy Stack.

## Slide 8
A WHO IS WHO
Real aggregators and platforms, and how big they are
VERIFIED
Source: Next Kraftwerke company page (Q4 2025); Kraken press release (23 Jan 2024); The Mobility House (Jul 2024); Nuvve quarterly releases (2025)
8
Company | What it is | Reported scale | Note
Next Kraftwerke | German virtual power plant operator | 15,541 MW networked; 14,375 units (Q4 2025) | Company page. Mostly not V2G
Kraken (Octopus Energy) | Software platform that runs flexible energy assets | Over 36 GW; 130,000 assets; 12 countries (Jan 2024) | Press release. Mostly not V2G
The Mobility House | EV and battery flexibility in Europe | 4,500+ EV batteries; 100 MW+ (Jul 2024) | Company statement
Nuvve | US company focused on V2G | 26.4 MW charging capacity managed (Q3 2025) | Capacity managed, not power exported
GreenFlex | Fictional aggregator in the DEG demand-flex example | Not a real company | Used later in this deck
Takeaway: aggregation is a mature business at gigawatt scale. Vehicle-based V2G is the newest and smallest slice of it.

## Slide 9
A WHO IS WHO
The standards: who talks to whom
REPORTED
Source: Open Charge Alliance, CharIN and vendor summaries; MoP EV charging guidelines, 17 Sep 2024 (clause 12; definition of UEI)
9
Standard | In plain words | Talks between | Layer
Beckn / UEI / DEG | The marketplace: find each other, agree terms, settle payment | Buyers and sellers | Market
OpenADR | Automated demand-response signals, e.g. reduce load 4 to 6 pm | Utility or market and aggregator | Market to aggregator
IEEE 2030.5 | Control messages to individual devices such as inverters and batteries | Aggregator or utility and devices | Aggregator to device
OCPP 2.1 (Jan 2025) | Open Charge Point Protocol. Now includes bidirectional and DER-control blocks | Charger and the operator's software | Charger to backend
ISO 15118-20 | Car to charger link, including two-way power transfer | Vehicle and charger | Vehicle to charger
India's 2024 EV guidelines (clause 12) recommend "UEI, OCPP, OCPI or open ADR" and define UEI as a network "based on open source Beckn Protocol".

## Slide 10
A WHO IS WHO
Nine terms, in plain words
Source: Definitions as used in the research; see Sources
10
Demand response
Paying users to change when or how much power they use.
Aggregation
Pooling many small resources into one bid.
Orchestration
The live software control that makes the pool behave as promised.
Virtual power plant (VPP)
A pool of small resources run as if it were one power plant.
V2G, V2H, V2X
An EV battery sends power back to the grid (V2G), a home (V2H), or anything (V2X).
Baseline
What a customer would have used anyway. Delivery is baseline minus actual use.
Reserve or ancillary services
Fast-response capacity kept on standby so the grid stays balanced.
Telemetry
Live meter and device data sent to the operator.
Shortfall or imbalance
The gap between promised and delivered energy. Usually charged.

## Slide 11
B AGGREGATION
Why one home's 1 kW does not count on its own
VERIFIED
Source: Amprion (balancing services); CERC Ancillary Services Regulations 2022, Reg. 7(1); FERC Order 2222, 85 FR 67094 (17 Sep 2020)
11
Germany
1 MW
Minimum bid in all balancing services (FCR, aFRR, mFRR). Amprion.
India, CERC 2022
1 MW
Minimum response for a secondary-reserve provider, on "standalone or aggregated basis". Also live telemetry to the regional control centre and a 30-second response.
USA, FERC Order 2222
100 kW
A grid operator may not set the minimum size of an aggregation above 100 kW.
1 MW is 200 cars at 5 kW each. Your one 1 kW home is the hairline on the left.
1 kW = 0.1% of the bar
each block = 10 cars; 20 blocks = 200 cars = 1 MW
Fixed costs such as metering, contracts and settlement do not shrink for a small unit, which is why markets set minimums. (Inference)

## Slide 12
B AGGREGATION
Many unreliable sources add up to one dependable block
EXAMPLE
INFERENCE
Source: Our own calculation (binomial model); not from a source. Real fleets are correlated, so a real aggregator would commit less
12
The assumption
1,000 EVs, 5 kW each
Each is plugged in and eligible on 60% of evenings
Independent of each other
Why it works
One car: 60% chance, unreliable
1,000 cars: about 600 available, and the number barely moves
So the pool can promise less than average and keep the promise
What the aggregator can promise (MW)
Expected supply
3.00 MW (600 cars)
Safe promise, 99% sure
2.82 MW
Safe promise, 99.9% sure
2.76 MW
To be 99% sure of a 1 MW bid, the aggregator needs about 370 enrolled cars,
not the 200 that 1 MW suggests. The gap is the safety margin.
Caveat: many drivers unplug at the same hour, so real availability moves together. A real aggregator commits less than this and watches it live.

## Slide 13
B AGGREGATION
How orchestration works, in seven steps
REPORTED
Source: Synthesis from Open Charge Alliance, CharIN, OpenADR and vendor summaries; DEG demand-flex devkit for baseline and settlement
13
1
Consent
The owner opts in and sets limits
2
Forecast
Who is plugged in, and how full
3
Offer
Commit below the expected total
4
Baseline
What each would have used anyway
5
Dispatch
Live signals to chargers and devices
6
Measure
Meter data, device by device
7
Settle
Pay for delivered, charge any shortfall
Aggregation is the pooling. Orchestration is steps 2 to 6 running live, every day.
Demand response is the wider idea. Aggregation and orchestration are how small resources take part in it.
A virtual power plant is the pool once it is orchestrated well enough to be sold like one plant.

## Slide 14
B AGGREGATION, WITHOUT V2G
DEG already prototypes aggregation: the demand-flex devkit
VERIFIED
Source: ies-devkit/devkits/demand-flex (README, uc1 bdr-w-baselining, uc2 bid-curve-pac). Guide status: Version 0.2, Draft / Non-Normative
14
TPDDL
Utility. The BPP. Publishes the flex need.
GreenFlex
Aggregator. The BAP. Discovers and commits.
1 Publishes need
2 Commits per slot
Enrolled meters
With EV chargers behind them. The real resources.
3 Enrols, controls
Settlement
Pay for delivered. Charge any shortfall.
4 Measured delivery
In the example
150 kW at ₹3.5/kWh
200 kW at ₹4.0/kWh
Shortfall penalty ₹1.5/kWh
Settles at ₹436.25
Scales to 10,000+ meters (paged); example cohort of 12,000
Battery level is used only to reconcile, never for payment
Roles are the same as our P2P demo: a BPP publishes, a BAP responds. The difference is that the aggregator's supply comes from many enrolled meters, not one seller.

## Slide 15
B AGGREGATION, WITHOUT V2G
How it settles: promised versus delivered
EXAMPLE
VERIFIED
Source: Formula: demand-flex-contractpolicy.rego (devkit). Rupee figures below are our arithmetic on the devkit's own price and penalty
15
The rule the devkit applies
delivered = sum over meters of max(0, BASELINE - USAGE)
pay = min(delivered, offered) x hours x PRICE
penalty = max(0, offered - delivered) x hours x SHORTFALL_PENALTY
net = pay - penalty
Read it as: you are paid for what you actually cut, up to what you promised. You are charged for the part you promised but did not deliver.
Worked example | Value
Offered | 200 kW for 30 minutes
Price / shortfall penalty | ₹4.0 / ₹1.5 per kWh
Actually delivered | 120 kW
Pay | 120 x 0.5 x 4.0 = ₹240
Penalty | 80 x 0.5 x 1.5 = ₹60
Net | ₹180
Compare our P2P demo: it already pays only for the reported delivery, but has no shortfall penalty.

## Slide 16
B AGGREGATION, WITHOUT V2G
Which IES use case covers plain aggregation? None yet
VERIFIED
Source: India-Energy-Stack/ies-accelerator (live repo, checked 23 Sep 2026); beckn/DEG devkits
16
Official IES use cases
Consumer Energy Passport
Consumer Meter Digest
DER Visibility
P2P Energy Trading
Smart Meter Data Exchange
DISCOM Regulatory Filing (draft)
Tariff Intelligence / Policy as Code (draft)
Nothing is named demand flexibility, aggregation or V2G
The closest, DER Visibility, is a DISCOM's view of resources behind its meters. Visibility only, not control.
But DEG already prototypes it
demand-flex devkit (draft v0.2): aggregator role, baselines, shortfall penalty
Also a draft "DR programme rules" sub-use-case in Policy as Code
So for our project
Plain aggregation: a devkit exists, not yet an official use case
V2G fleet: would extend that devkit, not start from zero

## Slide 17
C V2G
What V2G physically needs, from the car to the grid
INFERENCE
REPORTED
Source: ISO 15118-20 and OCPP 2.1 (Open Charge Alliance, CharIN summaries); DEG p2p-enrollment (DER_CONTROL consent)
17
EV battery
and a battery management system that allows discharge
ISO 15118-20
Bidirectional charger
can push power out, not only in
OCPP 2.1
Charge point operator
runs the charger's software
IEEE 2030.5
Aggregator
pools many chargers into one offer
OpenADR / Beckn
DISCOM or market
buys the block and pays
Three things must also be true before any discharge
Driver consent
The owner allows discharge and sets limits. DEG's schema has a DER_CONTROL consent for this.
Battery limits
Minimum charge to keep, and departure time, must cap what is offered.
Grid approval
The DISCOM must accept export at that connection.

## Slide 18
C V2G
The aggregator does not call drivers to a site
EXAMPLE
REPORTED
Source: EV fleet operator and VPP roles: ScienceDirect review of actors in EV integration. Numbers are an illustration
18
Common assumption
Drivers are asked to come to one place
They plug in there and power is collected
Feels like a physical gathering
What really happens
Every car stays where it normally is: home, office, depot
Each has its own two-way charger
The aggregator's software coordinates them remotely
Illustration: one evening
400
owners have signed up
250
are plugged in and above 30% charge tonight
5 kW
each, for 2 hours
1.25 MW
sold to the DISCOM as one block
The DISCOM talks to one aggregator. The particular 250 cars are different tomorrow, and only the aggregator has to care.

## Slide 19
C V2G
The actors in a V2G fleet, and where they sit in DEG
INFERENCE
REPORTED
Source: Actors and roles in EV VPP integration (ScienceDirect); mapping to BAP / BPP is our inference from the P2P and demand-flex designs
19
Real-world actor | What it does | Role in our architecture
EV owner | Opts in, gives standing consent, owns the battery | A resource behind the aggregator. Not its own seller
Aggregator (fleet operator) | Pools many EVs into one reliable, tradeable block | BPP: the seller side, like our seller-app but far larger
Charge point operator | Owns and runs the physical chargers | A technical layer beneath the aggregator
DISCOM (bulk buyer) | Needs a large, firm quantity at set times | BAP: like our buyer-app, asking for MW not kWh
Distribution grid operator | Checks the flow is safe for the local network | A policy and validation layer, like our discom allowlist rule
Genuinely new and hard
Turning hundreds of small, unreliable, changing sources into one firm number before any offer is published. The demand-flex devkit covers reduced consumption; vehicles exporting power are not yet modelled.

## Slide 20
C V2G
V2G outside India: why it exists and where it runs
REPORTED
VERIFIED
Source: BMW press (Feb 2026); The Mobility House (18 Nov 2025); Octopus (23 Jun 2025); Renault Group; PG&E (2025). Japan, Australia and the 1997 paper: secondary sources
20
Four purposes seen
Home backup (V2H)
Cheaper household energy
Grid stabilisation
Idle fleets as batteries
Where | What is running | Why | Scale | Status
USA, 1997 | Idea from Kempton and Letendre, University of Delaware | Value is "in responding when needed", not bulk power | Research paper | REPORTED
Germany | BMW with E.ON: first commercial home V2G offer (Feb 2026). Double grid fees abolished (Nov 2025) | Home and grid flexibility; makes V2G pay | First commercial offer | VERIFIED
UK | Octopus bundle: BYD Dolphin, bidirectional charger, smart tariff (Jun 2025) | Cheaper household energy | Consumer offer, run on Kraken | VERIFIED
Netherlands | "Utrecht Energized": V2G car sharing with Renault 5s | Grid stabilisation in a solar-rich city | 50 cars in service; 500 planned | VERIFIED
Japan | Home V2H sold since 2012, after the 2011 Fukushima disaster | Backup power at home | About 28,000 units by end 2024 | REPORTED
USA, California | Fremont schools: 14 electric buses, 6 bidirectional chargers | Idle buses as grid batteries | Fleet; export allowed (Rule 21) | VERIFIED
Australia | Amber and ARENA V2G trial | Household V2G trials | Target 50 chargers; A$3.2m | REPORTED
Pattern: Europe leads on commercial home offers, Japan on home backup, and the US on fleets. India's first demonstration came in May 2026.

## Slide 21
D RISKS
The three risks raised, and how markets handle them
REPORTED
VERIFIED
Source: PJM Manual 18, Rev. 62 (sections 4.8, 8.4A); imbalance settlement (Enlitia, secondary); DEG demand-flex policy; our P2P demo code
21
Accepted, but never supplied
Real markets: settle on metered delivery. Any gap is charged as an imbalance or penalty.
Our P2P demo: pays only for reported delivery. Demand-flex adds a shortfall penalty.
Missing: a penalty in P2P, and a credit check on the seller.
Hoarding offers to disturb the market
Real markets (PJM): offering new capacity needs a credit limit first, and a shortfall in an emergency is charged.
Our demo: a bid does not lock capacity. The seller reserves only when it accepts or counters.
Missing: a credit limit and buyer vetting.
The solar or vehicles fail
Real markets: a money question, not a blame question. The seller is unpaid for the shortfall and may pay imbalance charges.
Our system: settlement on the actual meter reading already fits this design.
Missing: force-majeure terms and insurance.

## Slide 22
E BOSCH AND INDIA
Bosch's public V2G level: the enabling layer
INFERENCE
VERIFIED
Source: Bosch Mobility (Vehicle Charge Communication Unit page); Bosch Research; Bosch Global Software Technologies India electrification page
22
Public and verified
Vehicle Charge Communication Unit supports CCS, GB/T, CHAdeMO and ChaoJi
Software functions listed: Plug & Charge (ISO 15118) and bidirectional power transfer per ISO 15118-20
"Vehicle to grid" listed as an optional feature
Research work on optimising bidirectional charging
No public evidence found
A named Bosch V2G pilot
An OEM partner for V2G
A Bosch aggregator or market service
Bosch India V2G activity. India's electrification page lists power electronics, e-machines, batteries and eAxles only
Our reading
Publicly, Bosch supplies the vehicle side: communication hardware and software, plus research
It is not shown running a market or an aggregation service
That is exactly the layer our proposal assumes already exists
Public sources stop here. Our own department may know much more, so check with the team before quoting Bosch's level to anyone.

## Slide 23
E BOSCH AND INDIA
India today: rules, one demonstration, and the meters
VERIFIED
Source: CERC Regulations 2022; MoP guidelines 17 Sep 2024; PIB (30 Mar 2026); RERC Regulations 2026 (gazette 15 Jun 2026); ISGF release (May 2026)
23
Jan 2022
VERIFIED
CERC Ancillary Services Regulations
Aggregated demand response may provide reserve. Needs 1 MW, telemetry, 30-second response.
17 Sep 2024
VERIFIED
Ministry of Power EV charging guidelines
Defines V2G and UEI. V2G "as per the requirements of the Distribution Licensee"; tariff set by the state regulator.
30 Mar 2026
VERIFIED
Smart meters (PIB)
6.13 crore installed overall, 4.69 crore under RDSS, against 20.33 crore sanctioned under RDSS. 7.24 crore reported by 30 Jun 2026.
17 Apr 2026
VERIFIED
Rajasthan Demand Flexibility Regulations
Discoms must hold flexible demand: 0.25% of peak (FY27), 1%, 1.5%, then 2% (FY30). Aggregators must register with the discom.
May 2026
VERIFIED
First V2G demonstration
ISGF with BSES Rajdhani, BSES Yamuna, TPDDL, ANERT. Four retrofitted Tata Nexon EVs.
Read left to right: the rules are arriving first, the vehicles and meters are still catching up.

## Slide 24
E BOSCH AND INDIA
What is still missing in India
INFERENCE
VERIFIED
Source: Sources on the previous slide; BIS standards compendium (ETD 51, June 2025); CEA standards pages. The tag on each card shows how sure we are
24
No V2G export price
Clause 18 of the guidelines leaves the V2G tariff to the appropriate state regulator. We found no figure set.
VERIFIED
Hard market access for small DERs
Aggregation is allowed, but reserve needs 1 MW, telemetry to the regional control centre and 30-second response.
VERIFIED
Aggregator rules differ by state
Rajasthan requires registration with the discom. We found no national aggregator framework.
INFERENCE
Metering
Baselines need interval data. By 30 Mar 2026 only 4.69 crore of 20.33 crore sanctioned RDSS meters were installed.
VERIFIED
Vehicles and chargers
The demonstration needed retrofitted cars, which suggests bidirectional EVs are not yet on sale.
INFERENCE
Standards: partly in place
BIS lists IS 17017 Part 23 (DC chargers), said to include bidirectional flow. ISO 15118-20 is not adopted, and no CEA rule covers V2G export.
VERIFIED

## Slide 25
F PROPOSAL
V2G fleet as an extension of demand-flex, not a new use case
PROPOSED
Source: Comparison of demand-flex, p2p-enrollment and ev-charging devkits and ElectricityCredential v1.2 (local files); our design suggestion
25
Already in demand-flex
Utility buyer (BPP) and aggregator (BAP)
Meters with EV chargers enrolled behind them
Baseline-based settlement
A shortfall penalty
Paging for 10,000+ meters
+
What V2G would add
Export in settlement. Today only reduced use is counted.
Battery-limited offers. Charge level and departure time cap the offer before commitment.
Per-driver discharge consent. DER_CONTROL exists but is not wired into the flow.
Moving assets. A car may charge at different meters.
Battery wear. No compensation is modelled.
Anchors in reality: India's first V2G demonstration (May 2026), Rajasthan's registered-aggregator rules (2026),
and the 2024 guidelines that already define V2G and UEI.

## Slide 26
F PROPOSAL
How a V2G fleet trade could run on Beckn
PROPOSED
Source: Our design suggestion, reusing the message shapes of the P2P and demand-flex devkits. Nothing here is built yet
26
What happens
Message or protocol
1
DISCOM publishes a flexibility need
Time window, MW wanted, price, shortfall penalty
catalog / publish
2
Aggregator discovers it
Filters for needs its fleet can meet
discover
3
Aggregator checks its fleet
Who is plugged in, charge level, consent granted
internal (OCPP data)
4
Offer below the expected total
MW per slot, sized for high confidence
init
5
DISCOM confirms
Terms locked, meters and cohort named
confirm
6
Dispatch and measure
Signals to chargers, per-vehicle readings
OCPP 2.1 / IEEE 2030.5
7
Report and settle
Delivered, shortfall, penalty, payment
status / on_status

## Slide 27
F PROPOSAL
Next steps and the questions to settle
PROPOSED
Source: Our suggested plan
27
1
Ask the Bosch team
What vehicle-side V2G capability is real today, and what can be shared
2
Draft the extension note
A short V2G-fleet proposal on top of demand-flex, in the same format as the UC3 pack
3
Prototype it
A simulated EV-fleet aggregator on our P2P base: battery limits, consent, shortfall penalty
4
Pick a pilot context
Delhi DISCOMs (where the demonstration ran) or Rajasthan (which has aggregator rules)
Open design questions
Export sign: how does settlement count power sent to the grid, beyond zero net use?
Consent: per drive, per day or standing? Who can revoke it, and how fast?
Battery wear: is it priced, and who decides the price?
Availability: how does the aggregator prove its forecast to the DISCOM before committing?

## Slide 28
EVIDENCE
How sure are we? A map of the evidence
Source: Statuses reflect the second verification pass, where the primary text was read wherever it could be reached
28
Read in the primary text
FERC Order 2222: 100 kW minimum cap
PJM: 100 kW to 5 MW per component; credit limit; non-performance charge
CERC 2022: 1 MW, 30 s, aggregated allowed
MoP guidelines 17 Sep 2024: V2G, UEI, clause 18
RERC 2026: targets, registration, incentives
Smart meters to 30 Mar 2026 (PIB)
DEG demand-flex formula; Bosch product page; Next Kraftwerke page
Secondary source only
7.24 crore meters by 30 Jun 2026
RDSS 25 crore target and 31 Mar 2028 end date
Nuvve FY2025 figure (28.3 MW)
Japan V2H unit count; Australia trial
1997 V2G paper (search summary)
German tax and meter rules after grid fees
Our inference
Pool statistics (370 cars for 1 MW at 99%)
Roles mapped to BAP and BPP
"Bosch is at the enabling level"
Aggregator rules differ by state
Bidirectional EVs not yet sold in India
The whole V2G-fleet proposal
Still open
A named Bosch V2G pilot or partner: none found publicly
Text of BIS Part 23 (paywalled)
Any CEA rule on V2G export: none found
Primary text for 7.24 crore, 25 crore and 2028
Whether demand-flex allows negative usage

## Slide 29
SOURCES
Sources (1 of 2): regulations, standards and programmes
29
Regulations and standards
FERC Order 2222, 85 FR 67094 (Federal Register)
PJM Manual 18, Rev. 62
PJM overview of FERC Order 2222
CERC Ancillary Services Regulations 2022
CERC Statement of Reasons (SOR-167)
MoP EV charging guidelines, 17 Sep 2024 (BEE mirror)
RERC Demand Flexibility Regulations 2026 (regulations page)
BIS standards compendium, ETD 51 (June 2025)
Amprion: balancing services (1 MW minimum)
PIB releases on smart meters: 2 Feb 2026 (PRID 2222217) and 30 Mar 2026 (PRID 2246897)
Programmes and operators
ISGF: South Asia's first V2G demonstration (PR Newswire)
Next Kraftwerke company page (Q4 2025 figures)
Octopus / Kraken press release (Jan 2024)
The Mobility House (Jul 2024)
The Mobility House: V2G progress by country
Nuvve quarterly results, Q1 to Q3 2025 (SEC / BusinessWire)
BMW and E.ON V2G launch (Feb 2026); Octopus V2G bundle (Jun 2025); Renault "Utrecht Energized"; PG&E Fremont school buses

## Slide 30
SOURCES
Sources (2 of 2): concepts, Bosch and DEG / IES
30
Concepts and background
Actors and roles in EV integration: VPP and fleet operator (ScienceDirect)
Imbalance costs explained (Enlitia)
Origin of V2G, University of Delaware (2021 article)
OCPP 2.1 announcement (Open Charge Alliance)
Kempton and Letendre (1997), Transportation Research Part D 2(3)
Bosch, DEG and IES
Bosch Mobility: Vehicle Charge Communication Unit
Bosch Research: electrified mobility
Bosch Global Software Technologies: electrification in India
India Energy Stack: ies-accelerator repository
beckn/DEG repository (devkits)
Local: ies-devkit/devkits/demand-flex, p2p-enrollment, ev-charging
Local: research-aggregation-bosch-v2g-india.md (full first-pass research record)