## Slide 1
PROOF OF CONCEPT · DEMONSTRATION PLAN
Can a Grid Ask an EV for Help —
and Get a Verified Answer?
A small, self-contained software demonstration of grid-to-EV flexibility,
coordinated through India's open digital energy network
Prepared for: Team Review | Direction & Scope Sign-off
Notes: Open with the question, not the acronyms. 'Can a grid ask an EV for help and get a verified answer' is the entire PoC in one sentence -- everything else in this deck explains how we'd show that, concretely.

## Slide 2
THE IDEA
A parked EV's battery is a mostly-idle resource
Grids need short bursts of extra power; EVs sit charged and unused most of the day
—
This is called Vehicle-to-Grid (V2G) — a car sends a little power back when the grid is stressed, and the owner gets paid for it
—
It's real and funded: the EU now requires new chargers to support this from 2027; real pilots are already running in China, the Netherlands, and the US
—
The open question for us: can India's own open energy network (IES, built on the Beckn protocol) actually coordinate this — discovery, agreement, and payment — end to end?
The Idea
2
Notes: Keep this to under a minute of talking. The real citations (EU mandate, real pilots) are in the appendix if anyone wants to dig in -- don't spend the room's attention on market data before they've seen what we'd actually build.

## Slide 3
THE DEMONSTRATION
What exactly we'll demonstrate
One concrete, end-to-end scenario — not a platform, not a framework
“A utility needs 5 kW of backup power for 30 minutes. A virtual EV, sitting at
80% charge, offers to help — and the whole exchange happens automatically.”
The requester — “Grid-Flex-Requester”
Represents the utility side. Says, in effect: “I need 5 kW of flexibility for the next 30 minutes.”
The provider — “V2G-Energy-Provider”
Represents an aggregator owning EV-001 — 60 kWh battery, 80% charged, able to safely spare 10 kWh at up to 5 kW.
The Demonstration
3
Notes: This is the single most important slide -- it's the whole PoC in plain language, with the two named actors we'll use consistently for the rest of the deck. Read the quote slowly.

## Slide 4
THE DEMONSTRATION
How the four pieces fit together
A fully self-contained system — nothing here depends on a real utility or a real car yet
GRID SIMULATOR
Generates the demand signal
GRID-FLEX-
REQUESTER (BAP)
Asks the network for help
V2G-ENERGY-
PROVIDER (BPP)
Owns EV-001, answers the ask
EV-001
(SIMULATED)
60 kWh · 80% charged
“I need 5 kW” → discovered over the real network → “EV-001 can help” → discharge simulated
The middle exchange — Grid-Flex-Requester discovering and contracting with V2G-Energy-Provider — runs over the real, live network. Only the grid demand and the EV's battery are simulated; the digital handshake between them is genuine.
The Demonstration
4
Notes: Point at each box left to right as you narrate the quote from slide 3. The callout box is important -- be precise that the MIDDLE step is real, only the two ends (grid demand, battery) are simulated.

## Slide 5
THE DEMONSTRATION
The actual conversation, step by step
Five real protocol actions, shown with this scenario's real numbers
discover
Grid-Flex-Requester
“I need 5 kW, for 30 minutes”
on_discover
V2G-Energy-Provider
“EV-001: 5 kW available, 10 kWh, consent ✓”
select / init
Grid-Flex-Requester
“I choose EV-001 — 5 kW, 30 minutes”
confirm
V2G-Energy-Provider
“Contract CONTRACT-001 is now active”
status
V2G-Energy-Provider
“FULFILLED — 2.5 kWh delivered”
The Demonstration
5
Notes: Read this top to bottom, slowly, in the room -- this IS the demo. Every one of these five lines becomes a real, visible, logged event when we actually run it.

## Slide 6
THE DEMONSTRATION
What success looks like on screen
GRID
Demand: HIGH · Flexibility requested: 5 kW
CONTRACT-001
5 kW × 30 min = 2.5 kWh · Status: ACTIVE → FULFILLED
EV-001 before
SoC 80%
80%
EV-001 after
SoC ≈ 75.8% · Delivered 2.5 kWh
76%
✓ FULFILLED
The Demonstration
6
Notes: This is the payoff slide -- the moment where the team sees the battery gauge visibly change and the status flip to FULFILLED. If the live demo works, this exact screen is what we'll actually show.

## Slide 7
SCOPE, STATED HONESTLY
What this proves — and what it doesn't
Digitally — yes, meaningfully
—
A real energy resource's constraints (battery, consent, timing)
—
Real discovery, agreement, and confirmation
—
Real, automatic settlement logic
—
The real open-network architecture, not a private API
Physically — no, and that's intentional
No real battery, inverter, or grid connection is involved. That requires real hardware, metering, and regulatory approval — a separate, later decision. We are calling this a “software-based V2G interoperability PoC,” deliberately not “a V2G system.”
Scope, Stated Honestly
7
Notes: This slide protects credibility. Be precise about the term we're using -- 'software interoperability PoC', not 'V2G system' -- if anyone in the room assumes we're about to plug in a real car, correct that here.

## Slide 8
SCOPE, STATED HONESTLY
Three separate layers — we're only building one
A common source of confusion, worth resolving upfront
A
Business layer (IES / Beckn)
Discovery + agreement — what THIS demo covers
B
Vehicle layer (ISO 15118-20)
How a real car and charger negotiate power — mature, open, already solved
C
Backend layer (OCPP)
How a charger reports to its backend — mature, open, already solved
Scope, Stated Honestly
8
Notes: We're demonstrating layer A only. Layers B and C already have real, open, working implementations elsewhere -- we're not reinventing car-charger communication.

## Slide 9
PLAN
Proposed roadmap — staged, each step checkable before the next
Stage 1
Register & connect
Stand up a real network identity; prove a basic real handshake works
Stage 2
Build EV-001
Author the simulated EV as a real, standard energy-resource object
Stage 3
Run the scenario
Execute the full discover → confirm → status flow from Slide 5, for real
Stage 4
Report honestly
Compare this approach against a conventional integration — either result is valid
Plan
9
Notes: Four stages, each a real gate -- we don't move to the next stage unless the previous one genuinely works.

## Slide 10
THE ASK
Approve a bounded technical evaluation
—
Approve 1-2 engineers, part-time, to build exactly the scenario on Slide 3
—
Approve minimal infrastructure spend
—
Review at a checkpoint before any further commitment
—
If it works: decide together what comes next
One concrete scenario. A real, checkable result — not a platform commitment.
Notes: Close here. The ask is deliberately scoped to exactly the one scenario in this deck -- not an open-ended platform build.

## Slide 11
APPENDIX
Terms & sources, for reference
Glossary
V2G = Vehicle-to-Grid. BAP/BPP = Beckn App/Provider Platform (requester/publisher roles). IES = India Energy Stack, India's open energy network, built on the Beckn protocol.
Sources
—
EU AFIR — bidirectional charging mandate from 1 Jan 2027
—
Real pilots: China (30 pilots/9 cities), Netherlands (Utrecht, commercial), US (Maryland V2G rules)
—
India Energy Stack — official documentation and accelerator repository
Appendix
11
Notes: One reference slide -- only go here if someone asks for a term definition or a source.