## Slide 1
LAYER B, DEEP DIVE · VEHICLE ↔ CHARGER PROTOCOL
How the EV Actually Talks to
the Charger — ISO 15118-20
The exact handshake, the signals exchanged, and the data fields and
values involved — the standard that makes real V2G physically possible
Prepared for: Team Review | Technical Deep Dive on Layer B
Notes: This deck answers the specific questions raised last time: what signals pass between EV and charger, what the handshake looks like, and what the actual data fields and values are. It stands alone from the PoC proposal deck.

## Slide 2
RECAP
Where Layer B sits in the bigger picture
Three separate conversations happen in any real V2G event — this deck is only about the middle one
A
Business layer (IES / Beckn)
Discovery + agreement between grid and provider — our PoC's layer
B
Vehicle layer (ISO 15118-20)
The EV and the charger negotiating power, in real time — THIS DECK
C
Backend layer (OCPP)
How the charger reports status/metering to its own backend system
Layer B is mature and standardized — already implemented by real vehicle and charger manufacturers today. Understanding it doesn't mean we build it; it means we know exactly what our PoC's simulated EV is standing in for.
Recap
2
Notes: Ground the room again: we are not building Layer B. We are learning it so we can speak to it accurately and know precisely what our simulated EV-001 represents.

## Slide 3
THE STANDARD
What ISO 15118-20 actually is
Published April 2022 by ISO/IEC — the current, official standard for EV ↔ charger communication
“Specifies the communication between the electric vehicle (EV) ... and the electric
vehicle supply equipment (EVSE) ... defines communication messages and sequence
requirements for bidirectional power transfer.” — ISO 15118-20:2022(E), Clause 1
The two endpoints, by name
EVCC — Electric Vehicle Communication Controller: the embedded system inside the car.
SECC — Supply Equipment Communication Controller: the embedded system inside the charger.
Why -20, not the older -2
ISO 15118-2 (2014) only supports charging. -20 (2022) is the first generation that formally defines Bidirectional Power Transfer (BPT) — the EV sending power back out. It's what makes real V2G possible at the protocol level.
The Standard
3
Notes: The quoted scope line is verbatim from the actual standard text (Clause 1) -- read directly from the ISO preview document, not paraphrased from a blog.

## Slide 4
THE HANDSHAKE
The whole journey, at a glance
Six stages from plugging in to power actually flowing — each one detailed on the following slides
1
Pair
SLAC — prove you're
plugged into THIS socket
2
Discover
SDP — find the charger's
address on the network
3
Secure
TLS + protocol version —
lock the channel
4
Handshake
Session, auth, services —
introduce & authorize
5
Negotiate
Charge parameters &
schedule — agree on power
6
Deliver
Power flows, then a
clean, checked stop
The Handshake
4
Notes: This is the map -- refer back to this slide's numbering as you move through the detail slides so the room doesn't lose the thread.

## Slide 5
STAGE 1 OF 6 — PAIR
SLAC — proving you're plugged into THIS socket
The charging cable itself carries a powerline signal (HomePlug GreenPHY); in a shared garage many cars may sit on the same physical network
DIRECTION
MESSAGE
WHAT IT DOES
EVCC→SECC
CM_SLAC_PARM.REQ
“Let's pair — here's my request ID”
SECC→EVCC
CM_SLAC_PARM.CNF
Returns a RunID and how many test “sounds” to expect
EVCC (bcast)
CM_START_ATTEN_CHAR.IND
“I'm about to send test pulses” — sent 3× for reliability
EVCC→SECC
CM_MNBC_SOUND.IND
A counted series of powerline “sound” pulses down the cable
SECC→EVCC
CM_ATTEN_PROFILE.IND
Reports the signal attenuation it measured per pulse
SECC↔EVCC
CM_ATTEN_CHAR.IND / .RSP
Charger sends the averaged attenuation profile; EV acknowledges
EVCC→SECC
CM_SLAC_MATCH.REQ/CNF
Finalizes the match — hands over a shared Network Membership Key
“SLAC” = Signal Level Attenuation Characterization. Sequence consolidated from public technical references (ISO 15118-3 / HomePlug GreenPHY) — exact vendor timing varies.
Layer B — ISO 15118-20
5
Result: EV and this one charger now share a private logical network (an NMK) — no other car on the same physical line can be confused with this one.
Notes: This is physical-layer pairing, not yet any V2G-specific content. It answers 'how does the charger know it's THIS car on THIS plug' in a facility with many chargers on one powerline segment.

## Slide 6
STAGE 2 OF 6 — DISCOVER
SDP — finding the charger's address
SECC Discovery Protocol: now that a private link exists, the EV still doesn't know the charger's IP address or port
STEP
MESSAGE / ACTION
WHAT IT DOES
EVCC
IPv6 SLAAC
EV self-assigns a link-local IPv6 address on the new private network
EVCC→(multicast)
SECC Discovery Request
UDP broadcast to a well-known multicast address, port 15118 — “who's my charger?” — states which security option (TLS / no-TLS) it wants
SECC→EVCC
SECC Discovery Response
Unicast reply: the charger's own IPv6 address + the TCP port to connect to, and confirms the security option
Port 15118 (UDP for discovery, then TCP for the session) is the IANA-registered port used across the whole ISO 15118 series.
Layer B — ISO 15118-20
6
Notes: Short stage, but a real gap most people skip past: the powerline pairing in stage 1 says nothing about IP addressing. SDP is the answer.

## Slide 7
STAGE 3 OF 6 — SECURE
Locking the channel before any real data moves
Everything from here on rides inside an encrypted, versioned, compressed envelope
TCP + TLS 1.3
The EV opens a TCP connection to the address/port SDP just returned, then performs a TLS 1.3 handshake. The charger presents a certificate the EV can verify up a real, audited chain of trust.
V2GTP
V2G Transfer Protocol — a small fixed header (version, payload type, payload length) wraps every message that follows, inside the TLS tunnel.
EXI
Efficient XML Interchange — every message is schema-defined XML, but sent as compact binary, not text. This is what actually crosses the wire, not raw XML.
SupportedAppProtocolReq / Res
The very first real message pair: the EV proposes which protocol namespaces it understands (e.g. urn:iso:std:iso:15118:-20:DC), ranked by priority; the charger picks one and confirms.
Layer B — ISO 15118-20
7
Notes: TLS 1.3 (RFC 8446) is a normative reference in the actual standard document -- this isn't an optional add-on, it's baked into the spec.

## Slide 8
STAGE 4 OF 6 — HANDSHAKE
Session, authorization, and service selection
Now that the channel is secure, the EV and charger introduce themselves and agree on what kind of session this will be
DIRECTION
MESSAGE
WHAT IT DOES
EVCC→SECC
SessionSetupReq
EV sends its EVCCID (its own identifier)
SECC→EVCC
SessionSetupRes
Charger replies with its EVSEID and a new SessionID
SECC→EVCC
AuthorizationSetupReq/Res
Charger states which authorization modes it supports — EIM (tap a card/app) or PnC (certificate-based, no user action)
EVCC↔SECC
AuthorizationReq/Res
EV actually authorizes — presents its PnC certificate signature, or the driver confirms via EIM
EVCC→SECC
ServiceDiscoveryReq/Res
“What can you offer?” — charger lists services: AC, DC, and crucially, whether Bidirectional Power Transfer (BPT) is among them
EVCC→SECC
ServiceDetailReq / ServiceSelectionReq
EV inspects and then formally selects DC + BPT for this session
Layer B — ISO 15118-20
8
Notes: The key moment for us is ServiceDiscoveryRes -- this is the message where the charger tells the EV whether it even supports discharge (BPT) at all.

## Slide 9
STAGE 5 OF 6 — NEGOTIATE
Two ways to negotiate power: Scheduled vs. Dynamic
Chosen during ScheduleExchangeReq/Res — this decision shapes everything that follows
Scheduled Control Mode
The EV and charger negotiate together: the charger proposes a whole power/price schedule up front, and the EV's own battery management system decides how to follow it.
Typical for public charging, where the vehicle is unpredictable.
Dynamic Control Mode — our scenario
“The SECC controls the power flow and gives the EVCC set points it should follow.”
— ISO 15118-20:2022(E), definition 3.16
An external system drives near-real-time decisions. This is the mode a grid-flexibility event like ours would actually use.
Layer B — ISO 15118-20
9
Notes: The Dynamic Control Mode quote is copied verbatim from the actual standard's own glossary entry (3.16) -- not a paraphrase. It maps directly onto our scenario: an outside system (our Grid-Flex-Requester, one layer up) is effectively the thing setting the pace.

## Slide 10
STAGE 5 OF 6 — NEGOTIATE
The actual fields — mapped onto our own scenario
DC_ChargeParameterDiscoveryReq/Res: the EV states its limits, the charger states its own
FIELD (real ISO 15118-20 name)
FROM
OUR EV-001 VALUE
EVMaximumDischargePower
EVCC
5,000 W
EVMinimumDischargePower
EVCC
0 W
EVPresentSOC
EVCC
80 %
EVEnergyRequest (this event)
EVCC
− 2.5 kWh
DepartureTime
EVCC
a future timestamp
EVSEMaximumDischargePower
SECC
5,000 W (charger's own limit)
Field names and their permitted ranges are real (per the -20 schema, powers are defined 0–200,000 W, currents 0–400 A). The specific values above are our own scenario's numbers, chosen to match the PoC — not worked examples copied from the standard, whose public preview doesn't include one. On the wire, each number is actually sent as a RationalNumber: value × 10^exponent, not a plain float.
Layer B — ISO 15118-20
10
Notes: This slide is the direct answer to 'what kind of parameters and values' -- be upfront in the room that the field names/ranges are verified real, but the specific numbers are our scenario's own, clearly labeled as such.

## Slide 11
STAGE 6 OF 6 — DELIVER
Power actually flows, then a checked stop
This is the loop that would physically run for our full 30-minute event — everything before this was setup
DIRECTION
MESSAGE
WHAT IT DOES
EVCC↔SECC
DC_CableCheckReq/Res
Insulation-resistance safety test on the DC cable before any real power flows
EVCC↔SECC
DC_PreChargeReq/Res
Charger ramps its output voltage to match the battery's present voltage — avoids an inrush current spike
EVCC→SECC
PowerDeliveryReq (START, discharge)
“Begin now” — and for BPT, explicitly signals the direction as discharge
EVCC↔SECC
DC_ChargeLoopReq/Res
The live heartbeat, repeating roughly every ~1s for the whole event: EV reports present SOC/voltage/current, charger reports its present output
EVCC→SECC
PowerDeliveryReq (STOP)
“Stop now” — the event is over, 2.5 kWh delivered
EVCC↔SECC
DC_WeldingDetectionReq/Res
Safety check confirming the contactors actually opened, not welded shut
EVCC↔SECC
SessionStopReq/Res
Clean, graceful termination of the whole communication session
Layer B — ISO 15118-20
11
Notes: DC_ChargeLoop is the one message pair that repeats -- everything else in this whole deck happens once per session. This loop is the actual live discharge.

## Slide 12
WHY THIS IS TRUSTWORTHY
Security isn't bolted on — it's a third of the document
TLS 1.3, mandatory
IETF RFC 8446 is a normative reference. Every application-layer message rides inside an encrypted tunnel — nothing is sent in the clear.
Certificate-based trust
The charger always proves itself with a certificate chained to a real, audited root CA; the EV optionally does the same for Plug & Charge (PnC), with zero driver action.
A genuinely large chunk of the standard
Clause 7.3, “Security concept,” alone runs about 35 pages — certificate profiles, key management, random number generation, firewall guidance.
Layer B — ISO 15118-20
12
Notes: Useful if anyone asks 'how do we know a rogue charger can't just claim to discharge a car it doesn't control' -- the standard's own security clause is the answer, and it's substantial.

## Slide 13
SCOPE, RESTATED
Where our PoC actually sits, relative to all of this
Nothing on the previous eleven slides is something we are building
—
Layer B (this deck) is mature, standardized, and already implemented by real vehicle and charger OEMs today. We are not modifying or reimplementing any of it.
—
Our PoC's simulated “EV-001” exists to stand in for what this whole handshake would report if it really happened: a state of charge before, an amount of energy delivered, a state of charge after.
—
Layer A (our actual PoC) only needs Layer B's outputs — a completed, verified discharge — to trigger discovery, agreement, and settlement over the open network.
Scope, Restated
13
Notes: Close the technical deep dive by reconnecting to the PoC deck's own honest-scope slide -- this prevents the room from concluding we now need to go build a 15118-20 stack.

## Slide 14
APPENDIX
Sources, for reference
Primary
—
ISO 15118-20:2022(E), “Road vehicles — Vehicle to grid communication interface — Part 20” — scope, definitions, and table of contents read directly from the standard
Secondary, corroborating
—
Typhoon HIL documentation — ISO 15118-20 DC/BPT message sequence and field ranges
—
CharIN e.V. — DC BPT ISO 15118-20 Interoperability Guide
—
Public technical references on SLAC / SDP behavior (ISO 15118-3, HomePlug GreenPHY)
Our own scenario's numeric values (5 kW, 60 kWh, 80% SoC, 2.5 kWh) are ours, not the standard's — clearly labeled as such throughout.
Appendix
14
Notes: Have this slide ready if anyone wants to go check a claim themselves.